## Slide 1: Laboratory safety
Tobias Christensen
Notes: ½

## Slide 2: Introduction
Create a safe and pleasant workspace across the laboratories
GLP – Good laboratory practice
Laboratory safety guidelines 2020
Studienet replaces safety compendium

## Slide 3: Accidents
Acute emergencies and fire call: 1-1-2
Not acute injuries that require treatment call: 18 18
  Opening hours: Weekday at 14-22 / Weekends and holidays at. 10-20
  Staff: Specially trained nurses
  Address: Kalundborg Sundheds- og Akuthus, Nørre Allé 31, 4400 Kalundborg (Call beforehand)
Insurance
Contingency plan
Teacher or L-AMU

## Slide 4: Fire
Restrict the fire if unable evacuate and call 1-1-2
Choose the right metode for fire fighting!
Fire blanket/ lab coat
Water/ emergency shower
CO2 extinguisher, present in all laboratories
Powder extinguisher present in KalA0.01, KalA0.02 & KalA0.05
Types of fire | Equipment | Location
Person or solid matter (not metal) | Emergency shower, water or fire blanket/lab coat | Entrance to laboratories, sinks and lab coat
Fluid, gas or equipment | Carbon dioxide extinguisher | Present in laboratories, look for the signs
Metal | Powder extinguisher | KalA0.01,02 & 05

## Slide 5: Work attire
Lab coat
  Pants
  Shoes
Eyes
  Contact lenses
  Glasses
  Safety googles
Hair
Jewelry
Gloves

## Slide 6: Safety 1
Hand wash (disinfection)
  When
  How
Gloves
  Material, expiration, quality approvals
  Secure/ false security?
  https://www.youtube.com/watch?v=t2xuszdLRko
Eye wash
Emergency shower
First aid

## Slide 7: Safety 2
Correct workspace
  No suction
  Table suction
  Fume hood
  Safety workbench
Pregnant or breastfeeding is exposed
  Inform us as fast as possible
  Safety precautions

## Slide 8: Safety 3
Behavior
Labels
  What, when, who (and APB label)
Ergonomics
Using the equipment
Fire sources
Stocks
  Protect the label
  Stored under suction

## Slide 9: Hazard and precaution (GHS)
H/P sentences and pictograms at the European commission’s webpage
Preparation
  Examine the regents
  Examine the safety precautions

## Slide 10: Hazards
Physical/ chemical
  H200
Health
  H300
Environment
  H400

## Slide 11: Precautions
General information
  P100
Safety
  P200
Safety procedure
  P300
Storage
  P400
Disposal
  P500

## Slide 12: (Material) Safety data sheet
Identification - product & producent
Hazards identification
Composition
First aid measures
Firefighting measures
Accidental release measures
Handling and storage
Exposure and personal protection
Physical and chemical properties
Stability and reactivity
Toxicological information
Ecological information
Disposal considerations
Transport information
Regulatory information
Other information

## Slide 13: Kemibrug – KBA and chemical info
https://www.kemibrug.dk/
SDS overview (KBA)
Applicability information
Toxicological information
Exposure and personal protection
Description of the substance
Fire fighting measures
Waste measures
First aid measures
Storage
Substitution

## Slide 14: Know the equipment!

## Slide 15: Cleaning
Garbage
  Various
  Chemicals
  Glass
  Biological
Cleaning
Laboratory washing
  Empty
  Rinse off
  Ethanol

## Slide 16: Dirty utensils
Dirty
  Empty
  Rinse off
  Ethanol
Clean
  Put in place
Glass pipettes
  Tip up!
  In the basket

## Slide 17: Evaporation
Organic chemistry
  Emptied into a waste container
  Rinsed with relevant solvent
    Water
    Ethanol
    Acetone
  Placed in a fume hood overnight for evaporation
Emptied chemical containers are evaporated as well

## Slide 18: Chemical waste groups
Group | Short description | Examples
O | Strong oxidizing agents and agents that react violently with water | Hydrogen peroxide, aluminum chloride
K | Contains mercury | Mercury batteries, mercury thermometer
Z | Packaging, medicine and batteries without mercury | Clinical waste and waste not suitable for other groups
T | Pesticides – Under normal circumstances not found in a lab | Toxins, pesticides
X | Inorganic substances | Acid, base, metal, salt
A | Minerals not containing emulsifiers – Under normal circumstances not found in a lab | Types of oils
B | Sulfur, fluorine, chlorine, bromine or iodine | Chloroform, PVC, sulfur
C | Liquid flammable agents (>18MJ/kg) | Acetone, ethanol, xylene
H | Organic waste with a high water content | Formalin, acetic acid, organic salts and acids

## Slide 19: Waste containers and labels
Plastic- or glass container?
  X, Y,Z / I , II , III?
  Ventilated lid?
Transport (ADR) – Who is allowed?
UN-number
Labels
  Chemical waste
  H350,H350i and H351
Contains agents which is regulated by the Danish work environment regulation regarding carcinogenic agents

## Slide 20: After lab
Handwash
Lab coat
  Dirty
  Wash
Always forgotten
Often forgotten

## Slide 22: Biological laboratories
Risk
  Treatment
Hygiene
  Hand wash
  Disinfection
  Lab coat
Cleaning
Disposal

## Slide 23: Sorting biological waste
Biological waste from GMO class 1 (solid) Biological waste from biological agents class 1 and 2 Human material – Tissue Needles, slides and other sharp objects | Clinical waste
Biological waste from GMO class 1 (Liquid) | Decontaminated and poured into the sink
Biological waste from GMO class 2 Biological waste from biological agents class 3 | Autoclaved
Uncontaminated packaging and utensils Autoclaved waste | Daily renovation

## Slide 24: Risk assessment
Be prepared !
Methods
  Risk
Chemicals
  Risk
    KRAN -> “CRAN”
    Substitution
    CAS-kemibrug
Cleaning
  Waste / CAS-kemibrug
Points of attention/ actions

## Slide 25: Good advice
Never pour water into concentrated acid!!! – Slowly pour the acid into the water while stirring.
Always turn the reagent tube opening away from yourself and other. Point it towards the back of the fume hood, it prevents splashing on people.
Sealed flasks or other glassware may never be heated due to the change of explosions.
Centrifuges is used according to the manual, always remember balancing the tubes.
Glass tubes may never be forced though a hole in a lid without knowing the right procedure!
Rube hoses that cannot be easily removed is cut off near the glass.
Vacuum equipment must be placed into a fume hood, if possible, due to the risk of implosions.
Dangerous chemicals (Toxic, corrosive, flammable) in glass flasks containing more than 1 liter, must be transported with curation, e.g. use a plastic container with a handle.
Fire may only be used where directed.
Flammable/explosive liquids and solids may never be used near fire – When heating use an electric heating plate / jacket.
Never pour chemicals back into the stock. Excess chemicals is treated as waste.
Liquids spills on stock bottles is rinsed with water and the bottle is wiped with tissue.
Chemicals is put back in their place immediately after use.
Solutions, you have created, must be labelled clearly! Contents, signature, date and pictograms.
Glass with abrasive (e.g. funnels) must be lubricated with silicone or a Teflon ring before use- Important when using bases.
Workspaces is kept clean and organized, utensils that are not in use in the current setup is kept at a distances – including laptops, notebooks etc.
Always handle a stock bottle by the label when pouring, this protects the label and prolong the lifespan.